## Slide 1: QGIS Tutorial
Kyle Cheung, Graduate Student
2019/07/16
Digital Agriculture Lab, UC Davis
kyhcheung@ucdavis.edu
https://github.com/kylezoa/gis-tutorial

## Slide 2: Tutorial Goals
Identify path/row for Landsat 8 images using Earth Explorer
Obtain public GIS files
Clip one shapefile with another shapefile
Change symbology or the appearance of a file
Perform raster calculation within a defined area
Calculate statistics of a defined area within a raster
*Download Landsat 8 images from Landsat on AWS

## Slide 3: Before Tutorial
Download and Install QGIS 3.4.9 LTR:
  http://qgis.org/downloads/QGIS-OSGeo4W-3.4.9-1-Setup-x86_64.exe
Download Landsat 8 Level-2 Product Images:
  https://ucdavis.box.com/s/1kwojur5m1tok1fj7uiep2ozcgl9qr2u
Register for Earth Explorer account:
  https://earthexplorer.usgs.gov
Download LandIQ Land Use data:
  ftp://ftp.wildlife.ca.gov/BDB/GIS/BIOS/Public_Datasets/2600_2699/ds2677.zip
Download Region of Interest .kml file:
  https://ucdavis.box.com/s/xqbzkbm8xythr0hg063iiee519bhhuas

## Slide 4: QGIS

## Slide 5: Area of Interest

## Slide 6: Data Resources
Brazil: https://github.com/juliohm/awesome-brazil-data
India: https://data.gov.in/
Thailand: https://github.com/pnphannisa/awesome-thai-gis
United States: https://uhcl.libguides.com/gis-data/GIS/data/us
European Space Agency (Sentinel): https://scihub.copernicus.eu/
US Geological Survey (Landsat): https://earthexplorer.usgs.gov

## Slide 7: Types of Data in GIS
Vector
Lines, coordinates, angles, polygons, vectors
Often used to draw boundaries
Geometrically based
Raster
Gridded data
Each grid points has a value
Images are raster data (hard to stretch it out or rotate it)
Often used to describe elevation, surface reflectance

## Slide 8: Types of Data in GIS
https://gis.stackexchange.com/questions/57142/what-is-the-difference-between-vector-and-raster-data-models

## Slide 9: Data Used
Landsat 8 Level 2 Surface Reflectance from Operational Land Imager (OLI)
  Each file contains a spectral band
  We will use Band 4 and Band 5 today
  Raster image

## Slide 10: Data Used
LandIQ Land Use Data
  Description of agricultural land use
  What is being grown on this field?
  Vector, shapefile

## Slide 11: Data Used
Region of Interest File (.kml, .kmz)
  A polygon drawn in Google Earth to denote an area of interest

## Slide 12: Satellite Imagery
https://www.usgs.gov/centers/eros/science/usgs-eros-archive-sentinel-2-comparison-sentinel-2-and-landsat?qt-science_center_objects=0#qt-science_center_objects
Landsat 8
  Description
    https://www.usgs.gov/land-resources/nli/landsat/landsat-science-products
  Data Access
    https://earthexplorer.usgs.gov
Sentinel-2
  Description
    https://earth.esa.int/web/sentinel/user-guides/sentinel-2-msi/resolutions/spatial
  Data Access
    https://scihub.copernicus.eu/

## Slide 13: Satellite Imagery
Identify path/row number for Landsat 8 images using Earth Explorer from USGS
  https://earthexplorer.usgs.gov
A path and row number describe a scene

## Slide 14
https://earthexplorer.usgs.gov

## Slide 15
https://earthexplorer.usgs.gov

## Slide 16: Satellite Imagery
ID: LC08_L1TP_042035_20190622_20190704_01_T1
https://prd-wret.s3-us-west-2.amazonaws.com/assets/palladium/production/atoms/files/LSDS-1574_L8_Data_Users_Handbook_v4.0.pdf

## Slide 17: Satellite Imagery
Level-1 Images are not corrected for atmospheric disturbances (haze, ozone)!
Use Level-2 images that contain surface reflectance values
We will use the files that I have uploaded to Box.

## Slide 18: Satellite Imagery

## Slide 19: Import Data

## Slide 20: Import Data

## Slide 21: Clipping Shapefiles
https://pro.arcgis.com/en/pro-app/tool-reference/analysis/clip.htm

## Slide 22: Clipping Shapefiles

## Slide 23: Clipping Shapefiles

## Slide 24: Clipping Shapefiles

## Slide 25: Clipping Shapefiles

## Slide 26: Change Symbology
Using color and symbols to show trends and label data

## Slide 29: Change Symbology

## Slide 30: Change Symbology
1. Select a category
2. Click Classify to show all categories in the selected data column

## Slide 31: Change Symbology

## Slide 32: Change Symbology

## Slide 33: Isolate a Feature Type
Each polygon is a “feature” in the shapefile.

## Slide 34: Isolate a Feature Type

## Slide 35: Isolate a Feature Type

## Slide 36: Isolate a Feature Type

## Slide 37: Isolate a Feature Type

## Slide 38: Isolate a Feature Type
Click on Fix geometries.

## Slide 39: Isolate a Feature Type

## Slide 40: Isolate a Feature Type

## Slide 41: Isolate a Feature Type

## Slide 42: Calculate NDVI
Normalized Vegetative Difference Index (NDVI)

## Slide 43: Calculate NDVI

## Slide 44: Calculate NDVI

## Slide 45: NDVI Statistics

## Slide 46: NDVI Statistics

## Slide 47: Display NDVI Statistics